## Slide 1
From Scripts to Systems
Day 2, Application Programming: SOLID, MVC and Threads
Building a real desktop application with PySide6

## Slide 2
Day 2 Welcome
Yesterday: script to objects to Adapter pattern to Strategy pattern
Today: SOLID principles, MVC, error handling, QThread workers, mini-app
By end of today: a working PySide6 desktop application

## Slide 3
SOLID in Instrument Code
Principles that prevent real problems

## Slide 4
Hardcoding Is a SOLID Violation
serial.Serial('/dev/ttyUSB0', 9600) — the class knows about deployment (SRP violation)
if format == 'csv': ... elif ... — adding a format means editing code (OCP violation)
gui_label.setText(reading) inside the driver — low-level depends on high-level (DIP violation)
These are not theory — they are real problems in real instrument code

## Slide 5
SOLID Violations in Code
class InstrumentDriver: def __init__(self): # SRP VIOLATION: knows about deployment details self.ser = serial.Serial('/dev/ttyUSB0', 9600) self.gui_label = QLabel() # and about the GUI! def read_and_save(self): raw = self.ser.readline() value = float(raw.split(b',')[1]) # OCP VIOLATION: adding JSON means editing here if self.format == 'csv': self.file.write(f"{value}\n") elif self.format == 'json': json.dump({"value": value}, self.file) # DIP VIOLATION: driver depends on Qt widget self.gui_label.setText(f"{value:.2f}")
Three violations, one class. Each makes the code harder to change, test, and reuse.

## Slide 6
SOLID in Practice
S — Single Responsibility: sensor reads, recorder writes, UI displays
O — Open/Closed: add new formats or devices by adding classes, not editing
L — Liskov Substitution: any adapter implementing the interface works
I — Interface Segregation: don't force a simple sensor to implement 20 methods
D — Dependency Inversion: depend on InstrumentAdapter, not serial.Serial

## Slide 7
Why Coupling Hardware to GUI Breaks Everything
Tightly coupled: button click calls serial.read(), blocks UI, frozen app
Testing: impossible without hardware plugged in
Reuse: impossible in a different UI or command-line tool
Error handling: one serial timeout crashes the entire application
If your button click handler calls serial.read(), you're one cable pull from freezing

## Slide 8
Coupled vs Decoupled
Coupled: GUI calls hardware
Decoupled: layers separated
class MainWindow(QMainWindow): def on_read_clicked(self): # GUI thread blocked until read completes ser = serial.Serial('/dev/ttyUSB0') ser.write(b'READ:TEMP\n') raw = ser.readline() # BLOCKS! value = float(raw.split(b',')[1]) self.label.setText(f"{value:.2f}") # Can't test without hardware # GUI freezes during read # Serial error crashes everything
class MainWindow(QMainWindow): def on_read_clicked(self): self.controller.start_reading() class Controller: def start_reading(self): reading = self.adapter.read_value('temp') self.view.display(reading) # Adapter is injected (real or simulated) # View only displays, never reads hardware # Controller orchestrates, owns nothing

## Slide 9
"The Controller Does Not Care" Architecture
The controller orchestrates — it does not know about:
serial ports (that's the adapter's job)
CSV files (that's the data sink's job)
Qt widgets (that's the view's job)
retry logic (that's the error handler's job)
This is the mantra of the course

## Slide 10
MVC for Instrument Applications
Model, View, Controller — separation that scales

## Slide 11
MVC — What It Means Here
Model: the data and state (current reading, connection status, recording state)
View: the PySide6 GUI (labels, buttons, plots)
Controller: the orchestrator (connects model to view, handles user actions)
MVC in instrument apps is looser than textbook MVC — the goal is separation

## Slide 12
Model, View, Controller — Code
# MODEL — pure Python, no Qt dependency class InstrumentModel: def __init__(self): self.current_reading: Optional[Reading] = None self.is_connected: bool = False self.is_recording: bool = False # If this class imports PySide6, something is wrong # VIEW — PySide6 widgets, displays only class MainWindow(QMainWindow): def display_reading(self, text: str): self.reading_label.setText(text) def set_status(self, status: str): self.statusBar().showMessage(status) # Does NOT call serial.read() or write files # CONTROLLER — wiring, the thinnest layer class Controller: def __init__(self, model, view, adapter): self.model = model self.view = view self.adapter = adapter # Connects button clicks to model actions
Model knows nothing about Qt. View knows nothing about hardware. Controller connects them.

## Slide 13
PySide6 Crash Course
QApplication, QMainWindow, QWidget — the application shell
Layouts: QVBoxLayout, QHBoxLayout, QGridLayout — arrange widgets
Widgets: QLabel, QPushButton, QComboBox, QStatusBar — display and input
Signal/slot: button.clicked.connect(self.on_connect) — event wiring

## Slide 14
PySide6 Minimal Window
import sys from PySide6.QtWidgets import (QApplication, QMainWindow, QLabel, QPushButton, QVBoxLayout, QWidget) class MinimalWindow(QMainWindow): def __init__(self): super().__init__() self.setWindowTitle("My First PySide6 App") # Create widgets self.label = QLabel("No reading yet") self.button = QPushButton("Read") # Layout layout = QVBoxLayout() layout.addWidget(self.label) layout.addWidget(self.button) container = QWidget() container.setLayout(layout) self.setCentralWidget(container) # Connect signal to slot self.button.clicked.connect(self.on_read) def on_read(self): self.label.setText("23.50 °C") app = QApplication(sys.argv) window = MinimalWindow() window.show() sys.exit(app.exec())

## Slide 15
Error Handling
Keeping the application alive when hardware fails

## Slide 16
Error Handling in Instrument Code
Instruments fail — cables unplug, serial buffers corrupt, timeouts happen
The question is not whether errors occur, but where and how you handle them
Timeout with default: try to read, return None after timeout
Retry with backoff: try N times, wait between attempts
Error propagation: adapter raises, controller catches, view shows status

## Slide 17
Error Handling Patterns
# PATTERN 1: Timeout with default def read_with_timeout(self, channel, timeout=2.0): self._serial.timeout = timeout try: raw = self._serial.readline() return self._parse(raw) except serial.SerialTimeoutException: return None # caller decides what to do # PATTERN 2: Retry with backoff def read_with_retry(self, channel, retries=3): for attempt in range(retries): try: return self.read_value(channel) except InstrumentError: time.sleep(0.5 * (2 ** attempt)) # 0.5s, 1s, 2s raise InstrumentError(f"Failed after {retries} retries") # PATTERN 3: Error propagation (adapter catches, controller receives state) # In the adapter: except serial.SerialException as e: self._connected = False raise InstrumentError(f"Connection lost: {e}")

## Slide 18
Safe Error Architecture
# LAYER 1: Adapter catches hardware exceptions class RealInstrumentAdapter(InstrumentAdapter): def read_value(self, channel): try: raw = self._serial.readline() return self._parse(raw) except serial.SerialException as e: self._connected = False raise InstrumentError(str(e)) # translated exception # LAYER 2: Controller receives application-level errors class Controller: def on_reading(self, reading): self.view.display_reading(reading.format()) self.view.clear_error() def on_error(self, message): self.view.show_error(message) # view shows status # App stays alive. No crash. No traceback. # The controller never sees SerialException. # The view never sees InstrumentError. # Each layer handles its own concern.
Each layer translates exceptions into its own vocabulary. No layer leaks implementation details.

## Slide 19
QThread + Worker: Background Acquisition
Keeping the GUI alive while reading hardware

## Slide 20
Why You Need a Worker Thread
Demo: GUI that calls serial.read() in the button handler — GUI freezes!
The GUI runs on the main thread (the Qt event loop)
Blocking the main thread means a frozen application and angry users
Solution: run acquisition on a separate worker thread

## Slide 21
Blocking vs Threaded
Blocking: GUI freezes
Threaded: GUI stays alive
class MainWindow(QMainWindow): def on_start(self): while self.running: # Runs on main thread! reading = self.adapter.read_value( 'temp' ) self.label.setText(reading.format()) time.sleep(0.1) # GUI cannot repaint # Buttons don't respond # Window shows "Not Responding" # User has to kill the process
class MainWindow(QMainWindow): def on_start(self): self.worker = AcquisitionWorker( self.adapter ) self.thread = QThread() self.worker.moveToThread(self.thread) # Signals cross thread boundary safely self.worker.reading_ready.connect( self.on_reading # runs on main thread ) self.thread.started.connect( self.worker.run ) self.thread.start() # GUI stays responsive!

## Slide 22
The Worker Class
from PySide6.QtCore import QObject, Signal class AcquisitionWorker(QObject): """Runs on a background thread. Communicates via signals only.""" reading_ready = Signal(object) # emits Reading error_occurred = Signal(str) # emits error message finished = Signal() # emits when done def __init__(self, adapter, interval=0.1): super().__init__() self.adapter = adapter self.interval = interval self._running = False def run(self): """Main acquisition loop. Runs on worker thread.""" self._running = True while self._running: try: reading = self.adapter.read_value('temperature') self.reading_ready.emit(reading) # -> main thread except Exception as e: self.error_occurred.emit(str(e)) # -> main thread time.sleep(self.interval) self.finished.emit() def stop(self): self._running = False
NEVER update GUI widgets from this class. Emit a signal, let the main thread handle display.

## Slide 23
Starting and Stopping Cleanly
class Controller: def start_acquisition(self): self.thread = QThread() self.worker = AcquisitionWorker(self.adapter) self.worker.moveToThread(self.thread) # Wire signals self.thread.started.connect(self.worker.run) self.worker.reading_ready.connect(self._on_reading) self.worker.error_occurred.connect(self._on_error) self.worker.finished.connect(self.thread.quit) self.thread.start() def stop_acquisition(self): self.worker.stop() # set _running = False self.thread.quit() # ask thread to exit self.thread.wait(5000) # wait up to 5 seconds # CRITICAL: always stop threads on window close def cleanup(self): if self.thread and self.thread.isRunning(): self.stop_acquisition() # prevent hang on exit

## Slide 24
Signal/Slot Communication
Signals are thread-safe in Qt — they cross thread boundaries safely
worker.reading_ready.emit(reading): controller runs on_reading on main thread
This is how data flows from worker to GUI without race conditions
Rule: NEVER update GUI widgets from the worker thread directly — always use signals

## Slide 25
Lab 5 — Worker Thread
Build an AcquisitionWorker that reads from SimulatedInstrumentAdapter
Connect it to a simple PySide6 GUI with Start/Stop buttons
Display readings in a QLabel via signals
Handle errors: show error in status bar, app stays alive
Critical: use QObject + moveToThread, not QThread subclass
Time: 35 minutes

## Slide 26
Lab 5 Debrief
Demo: working app with start/stop and live readings
Key test: what happens if the adapter throws an error?
Answer: error signal fires, GUI shows error, app stays alive
The GUI never freezes because acquisition is on a separate thread

## Slide 27
Mini-App Build
Putting it all together

## Slide 28
Mini-App — Putting It All Together
Build a complete instrument-control application with:
PySide6 GUI with MVC structure
SimulatedInstrumentAdapter (or real if you have hardware)
Worker thread for background acquisition
Start/stop controls and live reading display
Connection status indicator
Error handling throughout

## Slide 29
Lab 6 — Build the Mini-App
Phase 1 (10 min): review the labmonitor/ project structure
Phase 2 (15 min): understand the GUI, read ui/main_window.py
Phase 3 (15 min): understand the Controller, trace the flow
Phase 4 (15 min): run the application with python main.py
Phase 5 (15 min): modify something (display format, colour, title)
Phase 6 (extension): swap backend via config file
Time: 70 minutes total

## Slide 30
Day 2 Recap
Identified SOLID violations in real instrument code
Separated Model, View, and Controller concerns
Implemented error handling that keeps the application alive
Built a worker thread for background acquisition
Connected signals/slots across thread boundaries
Built a working PySide6 mini-app with live readings
Tomorrow: data architecture, file I/O, real-time plotting, performance