## Slide 1
From Scripts to Systems
Day 3, Data Architecture, Metadata and Performance
Where the data goes, how to keep it fast

## Slide 2
Day 3 Welcome
Yesterday: a working PySide6 application with MVC and worker threads
Today: where does the data go? How do we keep it fast?
By end of today: a complete instrument-control system with data logging and live plotting

## Slide 3
DataSink Abstraction
Decoupling data output from data production

## Slide 4
The Controller Does Not Care About Data Formats
The controller produces readings
It does not know whether they are written to CSV, JSON, HDF5, or /dev/null
Same architectural idea as the Adapter pattern, but for output
Controller sends to DataSink interface, implementations fan out

## Slide 5
The DataSink Interface
from abc import ABC, abstractmethod class DataSink(ABC): """The contract for all data outputs. Same idea as InstrumentAdapter, but for writing.""" @abstractmethod def open(self, metadata: dict) -> None: """Prepare the output (open file, write headers).""" ... @abstractmethod def write(self, reading: 'Reading') -> None: """Write a single reading.""" ... @abstractmethod def close(self) -> None: """Flush and close the output.""" ... # Three methods. That's the entire contract. # Adding a new format = adding one class.

## Slide 6
CsvSink vs JsonMetadataSink
CsvSink
JsonMetadataSink
class CsvSink(DataSink): def open(self, metadata): self._file = open(self._path, 'w') self._writer = csv.writer(self._file) self._writer.writerow( ['timestamp', 'channel', 'value', 'unit'] ) def write(self, reading): self._writer.writerow([ reading.timestamp.isoformat(), reading.channel, f"{reading.value:.4f}", str(reading.unit) ]) def close(self): self._file.close()
class JsonMetadataSink(DataSink): def open(self, metadata): self._path = self._generate_path() self._metadata = { 'experiment': metadata.get('name'), 'operator': metadata.get('operator'), 'instrument': metadata.get('instrument_id'), 'started': datetime.now().isoformat(), 'config': metadata.get('config', {}) } def write(self, reading): pass # metadata only, not per-reading def close(self): self._metadata['stopped'] = ( datetime.now().isoformat() ) with open(self._path, 'w') as f: json.dump(self._metadata, f, indent=2)
Same interface, completely different purpose. CsvSink writes data rows. JsonMetadataSink writes experiment context.

## Slide 7
CompositeSink — Writing to Multiple Outputs
class CompositeSink(DataSink): """The tee pattern: write to multiple sinks simultaneously.""" def __init__(self, sinks: list[DataSink]): self.sinks = sinks def open(self, metadata): for sink in self.sinks: sink.open(metadata) def write(self, reading): for sink in self.sinks: sink.write(reading) def close(self): for sink in self.sinks: sink.close() # Usage: write to CSV AND JSON metadata simultaneously sink = CompositeSink([ CsvSink("data/readings.csv"), JsonMetadataSink("data/"), # Add Hdf5Sink here later — no other code changes ])

## Slide 8
Lab 7 — Implement DataSinks
Review DataSink ABC, CsvSink, JsonMetadataSink, CompositeSink
Write a test script that creates a CompositeSink (CSV + JSON metadata)
Generate 20 readings using SimulatedInstrumentAdapter
Write each reading to the composite sink
Verify: CSV file has 20 rows, JSON file has metadata
Extension: add Hdf5Sink
Time: 30 minutes

## Slide 9
Writer Thread and Non-Blocking I/O
Decoupling acquisition speed from disk speed

## Slide 10
The Problem — File I/O Blocks Acquisition
Writing to disk is slow (especially CSV with flush)
If the writer blocks the acquisition loop, you miss readings
Solution: decouple with a queue and a dedicated writer thread
Acquisition thread puts on queue, writer thread takes from queue and writes to disk

## Slide 11
Coupled vs Decoupled I/O
Coupled: acquisition waits for disk
Decoupled: queue absorbs bursts
def acquisition_loop(self): while self.running: reading = self.adapter.read_value('temp') # BLOCKS: disk write stalls acquisition self.csv_file.write(reading.to_csv()) self.csv_file.flush() # If disk is slow, we MISS the next reading time.sleep(self.interval)
def acquisition_loop(self): while self.running: reading = self.adapter.read_value('temp') self.queue.put(reading) # instant, non-blocking time.sleep(self.interval) def writer_loop(self): while True: reading = self.queue.get() # blocks until data if reading is None: # sentinel: stop break self.sink.write(reading) # disk I/O here
The queue decouples speed: acquisition runs at instrument rate, writer runs at disk rate.

## Slide 12
Queue-Based Architecture
import queue import threading class WriterThread(threading.Thread): """Consumes readings from queue, writes to data sinks.""" def __init__(self, data_queue: queue.Queue, sink: DataSink): super().__init__(daemon=True) self.queue = data_queue self.sink = sink def run(self): while True: reading = self.queue.get() if reading is None: # sentinel value break self.sink.write(reading) self.sink.close() # clean shutdown # Setup data_queue = queue.Queue() writer = WriterThread(data_queue, composite_sink) writer.start() # Acquisition puts readings on queue (fast) data_queue.put(reading) # Shutdown: send sentinel, wait for writer to finish data_queue.put(None) writer.join()

## Slide 13
Lab 8 — Writer Thread
Add a queue.Queue between acquisition worker and data sinks
Create a WriterThread that consumes the queue
Read 50 values, put on queue, verify CSV output
Sentinel (None) for clean shutdown
Time: 20 minutes

## Slide 14
Units, Metadata and Configuration
Making data self-describing and experiments reproducible

## Slide 15
Units with Pint
from pint import UnitRegistry ureg = UnitRegistry() # Attach units to values — no more "is this Celsius or Fahrenheit?" temp = 23.5 * ureg.degC print(temp) # 23.5 degC print(temp.to(ureg.degF)) # 74.3 degF print(temp.to(ureg.kelvin)) # 296.65 kelvin # Where units belong in the architecture: # Adapter: attaches units to raw values # Model: stores unit-aware values # Sink: writes units to file # View: formats for display # In the adapter: def read_value(self, channel) -> Reading: raw = self._parse_response(self._serial.readline()) return Reading( value=raw * ureg.degC, # unit attached here channel=channel, timestamp=datetime.now() )

## Slide 16
Metadata for Reproducibility
Every data file should be traceable to:
who ran the experiment
what instrument was used
when it started and stopped
what configuration was active
what software version was running
If you can't reproduce the experiment from the metadata, the data is an orphan

## Slide 17
Configuration Files — YAML
default_config.yaml
Loading in Python
device: type: simulated # or "serial" port: COM3 # ignored if simulated baud_rate: 9600 acquisition: interval_ms: 100 channels: - temperature - voltage output: directory: ./data formats: - csv - json_metadata experiment: name: "thermal_test_001" operator: "J. Smith"
import yaml def load_config(path: str) -> dict: with open(path) as f: return yaml.safe_load(f) config = load_config("configs/default.yaml") # Config drives behaviour, no code changes adapter = create_adapter(config) sink = create_sinks(config) interval = config['acquisition']['interval_ms'] # Change the instrument? Edit YAML. # Change the sample rate? Edit YAML. # Change the output format? Edit YAML. # The code doesn't change.

## Slide 18
Lab 9 — Configuration and Metadata
Load default_config.yaml using config_loader
Create adapter and sink using factory functions
Connect, read 5 values, print them
Experiment: change device.type in YAML, observe the effect
Time: 20 minutes

## Slide 19
Performance Engineering
Finding and fixing the bottlenecks that matter

## Slide 20
The Six Most Common Performance Problems
1. Event loop blocking: serial.read() on main thread
2. Too many GUI updates: updating a label at 1000 Hz
3. Wrong-thread updates: writing to QLabel from worker thread
4. Slow file I/O in the acquisition loop
5. Slow parsing: regex in hot loops, string formatting per reading
6. No buffering: one-byte serial reads, one-row CSV writes

## Slide 21
Diagnosis and Fixes
# DIAGNOSIS: timing suspected hot spots import time t0 = time.perf_counter() reading = adapter.read_value('temperature') t1 = time.perf_counter() print(f"Read took {(t1-t0)*1000:.1f} ms") # DIAGNOSIS: queue health print(f"Queue depth: {data_queue.qsize()}") # If this number grows, the writer can't keep up # ALREADY SOLVED by our architecture: # [+] Event loop blocking -> worker thread # [+] Wrong-thread updates -> signals # [+] Slow file I/O -> writer thread + queue # REMAINING FIXES: # [ ] Too many GUI updates -> throttled QTimer # [ ] Slow parsing -> pure functions, avoid regex # [ ] No buffering -> batch writes, binary protocols

## Slide 22
GUI Update Throttling
# BAD: update view on every signal from the worker # At 100 Hz, this means 100 label.setText() calls per second def on_reading(self, reading): self.label.setText(reading.format()) # called 100x/sec! self.plot.add_point(reading.value) # 100 redraws/sec! # GOOD: throttle with QTimer at 30 Hz (smooth, efficient) def __init__(self): self._latest_reading = None self.display_timer = QTimer() self.display_timer.setInterval(33) # ~30 Hz self.display_timer.timeout.connect(self._refresh_display) self.display_timer.start() def on_reading(self, reading): self._latest_reading = reading # just store it (fast) def _refresh_display(self): if self._latest_reading: self.label.setText(self._latest_reading.format()) self.plot.update() # one redraw at 30 Hz
One change: 100 redraws/sec drops to 30. GUI goes from jerky to silky smooth.

## Slide 23
Real-Time Plotting with PyQtGraph
Fast, Qt-native, designed for live data

## Slide 24
Why PyQtGraph, Not Matplotlib
Matplotlib: excellent for static plots, too slow for real-time updates
PyQtGraph: designed for real-time, Qt-native, 60+ FPS updates
Embeds directly in PySide6 layouts, just add to a QVBoxLayout
If your plot flickers or lags, you're using the wrong library

## Slide 25
Efficient Real-Time Plotting
import numpy as np import pyqtgraph as pg class LivePlotWidget(pg.GraphicsLayoutWidget): """Dual-channel real-time plot with ring buffer.""" def __init__(self, buffer_size=500): super().__init__() self.buffer_size = buffer_size self.buffers = { 'temperature': np.full(buffer_size, np.nan), 'voltage': np.full(buffer_size, np.nan), } self.index = 0 # Two plots, linked X axes self.temp_plot = self.addPlot(row=0, col=0, title="Temperature") self.volt_plot = self.addPlot(row=1, col=0, title="Voltage (V)") self.volt_plot.setXLink(self.temp_plot) self.temp_curve = self.temp_plot.plot(pen='#4FC3F7') self.volt_curve = self.volt_plot.plot(pen='#FFB74D') def add_value(self, value, channel): buf = self.buffers[channel] buf[self.index % self.buffer_size] = value self.index += 1 def refresh(self): """Call at 30 Hz from QTimer, NOT per-reading.""" for channel, curve in [('temperature', self.temp_curve), ('voltage', self.volt_curve)]: curve.setData(self.buffers[channel])

## Slide 26
Lab 10 — Real-Time Plot
Add a dual-channel PyQtGraph plot to a PySide6 window
Use SimulatedInstrumentAdapter to generate temperature and voltage data
Ring buffer (numpy array, 500 points per channel)
QTimer at 30 Hz reads from adapter and updates both traces
Start/Stop buttons, smooth scrolling traces
Time: 30 minutes

## Slide 27
Capstone Integration
Putting every piece together

## Slide 28
Everything Connected
Your LabMonitor application now has:
MVC architecture with clean separation
Simulated and real adapters (interchangeable)
Measurement strategies (swappable)
Background acquisition worker (QThread)
Data queue plus writer thread (non-blocking I/O)
CSV and JSON metadata sinks (extensible)
Configuration-driven behaviour (YAML)
Real-time PyQtGraph plotting

## Slide 29
Cross-Course Themes — Adding Features
# NEW MEASUREMENT MODE? Add a Strategy class. class BurstReadStrategy(MeasurementStrategy): def execute(self, adapter) -> list[Reading]: ... # Files changed: 1. Everything else: untouched. # NEW DEVICE? Add an Adapter class. class ModbusAdapter(InstrumentAdapter): def connect(self): ... def read_value(self, channel): ... # Files changed: 1. Everything else: untouched. # NEW DATA FORMAT? Add a DataSink class. class Hdf5Sink(DataSink): def open(self, metadata): ... def write(self, reading): ... # Files changed: 1. Everything else: untouched. # NEW CONFIG OPTION? Edit YAML. # Files changed: 0 (code). 1 (config).

## Slide 30
What Comes Next
Testing: start with smoke tests, grow from there
Packaging: PyInstaller for distributable applications
Version control: Git for team collaboration
CI/CD: automated testing on commit
Documentation: docstrings where they matter, not everywhere

## Slide 31
Course Complete
Day 1: Script to Objects to Adapter to Strategy
Day 2: SOLID to MVC to Error Handling to QThread to Working Application
Day 3: DataSink to Writer Thread to Config to Performance to Live Plotting
Key mantra: the controller does not care
Add new things by adding classes, not by editing existing code
Architecture makes the swap possible, configuration makes it easy

## Slide 32
From Scripts to Systems
Feedback and questions welcome